## Slide 1: CAESAR: Characterizing and Understanding Atmospheric Boundary Layer Fluxes, Structure and Cloud Property Evolution in Arctic Cold Air Outbreaks
Instruments
MARLi: No changes
Airborne Doppler Lidar (ADL): From nadir only to a five-beam system
Zhien Wang and Flynn Mcginnity
University of Colorado, Boulder and Stony Brook University (Starting at Sep. 1st)
and
John Cassano and TBD
University of Colorado, Boulder

## Slide 2: The Synergy of Raman and Doppler Lidar Measurements
Raman Lidar
Water vapor, temperature, and aerosol profiling
Wind and Turbulence profiling
Five Fixed-beam Airborne Doppler Lidar (ADL)
Sensible and Latent heat flux profiles from below cloud legs.
Notes: Advancing Future PBL Observations
Space-based PBL observations will be limited and take time.
Airborne simultaneous measurements of Dynamics and thermodynamics are essential for PBL processes study.
True mobile measurements to deal with spatial heterogeneity.

## Slide 3: Raman Lidar Measurement Validation
CHEESEHEAD In Situ Measurements
Mean T difference: -0.7 K
Mean WV difference: 0.15 g/kg
T
WV
In Situ
CRL
SWEX Dropsonde Measurements
1
2
3
4
5
Mean T difference:
-0.34K
Mean WV difference:
0.06 g/kg
Raman lidar can provide reliable water vapor and temperature measurements within PBL!

## Slide 4: Lidar-radar Synergy for Cloud Structures and Properties
Cloud and Precipitation structures
Cloud phase vertical distributions
Mixed-phase cloud properties